## Slide 1: Scheduling & Forecasting in Rajasthan INITIATIVE of IWTMA CEA Meeting on furnishing Real Time Generation 04.05.2018
INDIAN WIND TURBINE MANUFACTURERS ASSOCIATION

## Slide 2: Scenario of Rajasthan- 2016
Only partial Forecast data available with SLDC.
SLDC not equipped for analysis of deviation between scheduled wind power and actual injection
No Data integration system in between pooling substations and SLDC for getting the details of Power injection at any time.
SLDC used to get data on phone and manually maintain a log book, which is not reliable as the data is received at different times, hence are not comparable.
Availability of actual data of Injected Power is possible only after 30 days from the MRI record.
SLDC is in the process of installing Fibre optic communications from Pooling Sub Stations to Inter connection Substations, which will take around 4 years.

## Slide 3: Forecasting & Scheduling – Coordination by IWTMA
IWTMA is playing a role as a single co-ordinating agency for compiling all data as received from various developers / generators and forwarding to SLDC.
Approx 4246 MW Zero revision forecast data on Day ahead basis is being forwarded to SLDC before 10:30 AM daily. This is followed by 16 revisions as per regulations
IWTMA engaged REConnect Energy as System Integrator for making the exercise dynamic and analytical.
System Integrator will be responsible for installing ABT meter with Dual SIM based GPRS Modem in all the polling substations. The modems will work on storage & forward concept.
System Integrator will also install RTUs in pooling substations with a dedicated Gateway at SLDC to synchronize all RTUs in SLDC System as per their requirement.

## Slide 4
Suzlon
Gamesa
WWIL
ReGen
Inox
IWTMA
Uninterrupted submission to SLDC
Consolidate Day ahead, Zero
revision Forecasting at 10.30 AM
16 Revisions as per regulations
Forecasted Data received at SLDC
Present Status
4
IPP’s

## Slide 5
Substation 1
ABT Meter with
Duel SIM based GPRS Modem
Substation 2
ABT Meter with
Duel SIM based GPRS Modem
Substation 3
ABT Meter with
Duel SIM based GPRS Modem
Substation “N”
ABT Meter with
Duel SIM based GPRS Modem
System Integrator (Data Collection
Aggregation, Analytics and MIS for
Association, all Stakeholders & SLDC)
Gamesa
ReGen
Suzlon
Inox
SLDC
5
Working Architecture : For ABT Meter Data Acquisition & Role of System Integrator
Actual Generation
Forecast Data
Forecast Data
Forecast Data
Consolidated Forecast with all Revision
IWTMA
IPP’s
Wind World

## Slide 6
Substation 1
RTU & cellular module with Dual SIM card
Substation 2
RTU & cellular module with Dual SIM card
Substation “N”
RTU & cellular module with Dual SIM card
IPP’s Substation
RTU & cellular module with Dual SIM card
Gateway/Inter-phasing Equipment/Router at the SLDC for picking the data from different RTUs
SLDC system
IEC 104 protocol
6
Real time data
Data Transfer Architecture : From RTU to SLDC
Real time data
Dedicated
Lease
Line

## Slide 7: Scope of System Integrator
Maintain the Communication system for transfer of data from ABT meters to Developer/Generator and SLDC .
Maintain the RTU/Data Acquisition System and Gateway/Inter-phase equipment at the SLDC.
Compilation of forecast data including all Revisions, as per regulation and submit to SLDC.
Co-ordination with SLDC, RDPPC, Sub Stations, Developers / Generator or any other designated agency
Prepare periodic Reports covering Analysis, issues of curtailment, Actual Vs Forecasted Deviation etc.
Reports and Management Information System for SLDC /OEM/
Developers/Generators or any designating agencies.

## Slide 8: Status as on Date (Hardware & Software)
ABT Meters (L&T Make) and Dual Modems (iMDAS by REConnect Energy) installed at all Pooling Substations and streaming real-time data to SLDC
RTUs installed with dual-modem and some of the pre-existing RTU’s are streaming data to dedicated wind energy gateway installed as SLDC
7 different OEMs being integrated into the system from the hardware and software point of view (Suzlon, WWIL, ReGen, INOX, Gamesa, Greenko, Tata/Welspun)
SLDC Rajasthan and IWTMA having a real-time access to data (static and power) through a state-of-the-art web-application (GRID Connect). Each other stakeholder has access through password for their own data

## Slide 9: Status as on Date (Forecasting & Scheduling)
Forecast - Aggregation & Scheduling
  Data received from multiple forecasters is being aggregated and sent to SLDC
  Daily 36 PSS (4246.75MW) are sending day-ahead forecasts
  Daily 36 PSS (4246.75MW) are sending intra-day forecast revisions
  (16 revisions)
Real time Generation Data
    Daily 3456.35 MW actual generation data is beamed to SLDC through Gateway installed at SLDC. The work is in progress for the balance capacity of 790.4 MW

## Slide 10: Reports Generation and Download options
Following reports can be downloaded from the portal, in Excel (csv) & PDF
Format. Can also be Copied & Printed
Current Day's Aggregated Day Ahead Forecast, Revised Forecast and
Actual Power Generation
Next Day's Day Ahead Forecast Pooling Sub Station wise.
Historical Aggregated Revised Forecast and Actual Power with date selection option.
Current Day's Region wise Aggregated Revised Forecast and Actual Power Generation
Pooling Sub Station wise Forecast Vs Actual generation
Static Details Pooling Sub Station wise with project status.

## Slide 11: Web-application (real-time FC vs. Actual state level)

## Slide 12: Web-application (regional break-up of actual generation)

## Slide 13: Web-application (DA forecast with each PSS level breakup)

## Slide 14: Web-application (Historical data and accuracy MIS)

## Slide 15: Web-application (PSS level f/c vs. actual comparison)

## Slide 16: Deadlock in the project on S & F in RAJASTHAN
The implementation of the project undertaken by IWTMA is almost complete and the data is visible and accessible by SLDC Rajasthan.
But, the project is at risk of shutting-down due to the NON-PAYMENT (opex) of dues by wind generators.
Reconnect has approached IWTMA for the solution and the payment of 80 Lakhs on account of O&M.

## Slide 17: Deadlock in the project on S & F in RAJASTHAN
  The argument of the wind generators is that now forecasting and scheduling regulations are in place and with the appointment of QCA by the generators, the services of this this project are no longer required .
However, they are missing on very critical point:
  “That this project provides real-time generation data to SLDC and they are obliged to provide the data to SLDC. Also without RTGD, the existing problem of backing-down will not go away and the Deviation Mechanism cannot be verified by the Generators resulting in the financial losses to them.”

## Slide 18: THANK YOU..
  O.P.Taneja , Associate Director
  Indian Wind Turbine Manufacturers Association
  Transit House: B6/65, Safdarjung Enclave,
  New Delhi - 110 029, India
  Tel: +91 114181 4755, 4181 4744 Mobile: +91-9971096623
  www.indianwindpower.com

## Slide 19
INSTALLED CAPACITY OF WIND POWER IN RAJASTHAN |  |  |  |  |  | As on 31/04/2017
Developer | Jaisalmer | Jodhpur | Sikar | Barmer | Chittorgarh/ Pratapgarh | Total
RRECL | 45.4 | 2.1 |  |  | 2.25 | 49.75
Suzlon | 1608.95 | 315.5 |  | 9.6 |  | 1934.05
WWIL | 896.77 | 98.4 | 7.2 |  |  | 1002.37
NEPC | 0 |  |  |  | 0.675 | 0.675
RRB | 25.8 |  |  |  |  | 25.80
Veer | 76.5 |  |  |  |  | 76.50
Regen | 0 |  |  |  | 211.5 | 211.50
Inox | 554 |  |  |  |  | 554.00
Welspun | 0 |  |  |  | 126 | 126.00
Gamesa | 0 |  |  | 40 |  | 40.00
Mytrah | 62.9 |  |  |  |  | 62.90
Tanot | 120 |  |  |  |  | 120.00
Rajgarh | 74 |  |  |  |  | 74.00
Others |  |  |  |  | 15 | 15.00
Total | 3464.32 | 416 | 7.2 | 49.6 | 355.425 | 4292.545