## Slide 1
TELANGANA STATE LOAD DESPATCH CENTRE
TSTRANSCO
Notes: 1

## Slide 2: Data Integration Architecture for RE Generators
The real time operational data communication from renewable energy sources to SLDC is broadly categorised as
Generators connecting at 132kV Voltage Level and above
Generators connecting at 33kV Voltage level and below

## Slide 3: Generators connecting at 132kV Voltage Level and above
The data acquisition of generators connecting at 132 KV Voltage level and above is being done through PLCC / fibre on IEC 101 and 104 protocols necessitating Substation Automation System (SAS) at the plant end.
It is made mandatory for all the generators to establish data connectivity to SLDC before synchronisation of the plant.
Further, the generator is made to transmit data up to the nearest data collection point (wideband location) from where data is communicated to SLDC over existing communication network.

## Slide 4: Generators connecting at 33KV voltage level and below
For Discom embedded Renewable energy generators (except roof top solar) connecting at 33 KV Voltage level and below, the plant data is being transmitted to SLDC through Leased Line over MPLS on IEC-60870-5-104 protocol in secured VPN network.
For ensuring reliable data, it is made mandatory to have KEMA certification for IEC 101 and 104 protocols for the RTUs to be erected at Plant end. SLDC will approve the DAS equipment to be installed at Plant end. The plant will be permitted to synchronize only after SLDC clearance is issued.
The HUBs of BSNL, AIRTEL, IDEA and RELIANCE service providers were established at SLDC facilitating RE Generators to choose any of these service providers as a medium for data integration to SLDC.
For communicating with plant directly, IP phone installation at plant has been made mandatory

## Slide 6
Sl.No | Voltage level | No. of Generators | Solar (MW) | Wind (MW) | Total (MW) | Integrated with SLDC | % Integrated with SLDC
1 | 220 KV | 7 | 708 | 0 | 708 | 708 | 100
2 | 132 KV | 37 | 1409.9 | 100.8 | 1510.7 | 1510.7 | 100
3 | 33 KV | 119 | 1141.3 | 0 | 1141.3 | 923.9 | 81
4 | 11 KV | 5 | 4.75 | 0 | 4.75 | 0 | 0
Total |  | 168 | 3263.9 | 100.8 | 3364.7 | 3142.6 | 93.4%
RE Data Integration with SLDC
The real time data is established upto inverter block level for all the RE generators.
The control feature upto inverter block level is enabled.

## Slide 8
Imposing Grid Discipline
The data loss from RE generators for a continuous period of one week will be recommended for stoppage of bills till data is restored.
By implementing these measures data availability has improved to a great extent.

## Slide 9
THANK YOU