## Slide 1
Renewable Energy Generation Data Availability

## Slide 3
As per data furnished by respective SLDCs.

## Slide 4
As per data furnished by respective SLDCs.

## Slide 5
Telemetry Issues
Sudden jumps in value which distorts real time trends as well as data archives.
These issues are quite frequent as far as renewable data telemetry is concerned.

## Slide 6
Telemetry Issues
Incorrect Solar Generation (data freeze) during night or early morning hours.

## Slide 7
Real-Time Data Telemetry Requirement
Wind turbine generating plants
Turbine Generation (MW/MVAR)
Wind Speed (meter/second)
Generator Status (on/off- line)-this is requires for calculation of availability of the WTG
Wind Direction (degrees from true north)
Voltage (Volt)
Ambient air temperature (deg. C)
Barometric Pressure (Pascal)
Relative humidity (in %)
Air Density (kg/m3)
For Solar generating plants
Solar Generation Unit/ Inverter-wise (MW and MVAR)
Voltage at interconnection point (Volt)
Generator/Inverter Status (on/off-line)
Global horizontal irradiance (GHI)-Watt per meter square
Ambient Temperature (o C)
Diffuse Irradiance- Watt per meter square
Cloud Cover- (Okta)
Direct Irradiance- Watt per meter square
Sun-rise and sunset Timing
Rainfall (mm)
Relative humidity (%)
Performance Ratio
As per
Procedure for implementation of the framework on forecasting, scheduling and
imbalance handling for renewable energy (RE) generating stations including power parks based on wind and solar at inter-state level
issued by CERC dated 3rd March, 2017.

## Slide 8: Discussions- Real Time data availability
All data should be integrated with SCADA available at RLDC/SLDC
Modality to be finalised for data integration with SCADA
Communication media should be as per Technical Standards of communication for Power Sector being prepared by CEA.

## Slide 9
Thank you

## Slide 10
All India Solar Generation

## Slide 11
All India Wind Generation

## Slide 12
SCADA Snapshot of Renewable Energy Generation of Maharashtra State Electricity Transmission Co. Ltd.

## Slide 13
SCADA Snapshot of Renewable Energy Generation of Gujarat State Load Despatch Centre

## Slide 14
As per SCADA Data at NLDC
Wind Generation for Northern Region

## Slide 15
As per SCADA Data at NLDC

## Slide 16
As per SCADA Data at NLDC

## Slide 17
As per SCADA Data at NLDC

## Slide 18
As per SCADA Data at NLDC

## Slide 19
As per SCADA Data at NLDC

## Slide 20
As per SCADA Data at NLDC

## Slide 21
As per SCADA Data at NLDC

## Slide 22
As per offline Data reported at NLDC

## Slide 23
As per offline Data reported at NLDC

## Slide 24
As per offline Data reported at NLDC

## Slide 25
As per offline Data reported at NLDC

## Slide 26
As per SCADA Data at NLDC

## Slide 27
As per SCADA Data at NLDC

## Slide 28
As per SCADA Data at NLDC

## Slide 29
As per SCADA Data at NLDC

## Slide 30
As per SCADA Data at NLDC